5900 Service and Maintenance

operation notes

Similar to original Rowe 5900 board.

Mode:         Display		Active Keys

Service:       Time and day	.25 payout

.10 payout

.05 payout

Exit with door switch		Mode = enter maintenance mode

Maintenance:   “MAINT”	0,3,5,7, 8, reset

0 -Motor	   “MOTOR”

enter either a selection # or 00 or 99 to run all motors.

Price is displayed during run. Reset or door to exit.

3 -Set price        “SET PRICE”   $12.75 = unset price

Enter Selection, reset, or door to exit.

If selection   1 = up price 2 = down price

9 = accept price & next selection.

0 = skip to next selection

5 -Sales meter	      Sales value

Exit with reset or door close.

7 -Set time 	    “CLOCK”	selection # or reset

5 clock set     display shows   “DAY  HRMINA/P”

1 day up     2 hr up	3 min up	4 AM/PM

5                 6 hr dn	7 min dn

9 accept

6 lockout

8-Gum Row         “GUM ROW  x”        (for Tru-vend optics system)

1 toggle shelf 8 or 9

9 Accept               0 Reset

John Wick      Greenwick Inc.       610-857-5910 ET