4900 2 and 3 board installation

Take a moment to study the replacement board looking for connectors labeled 3B. Install the 6 standoffs in the board. You may want to label the connectors as you remove them from the old boards.

Locate these connectors on the replacement board:

- Display  P9

- Motors P1 and P2. Observe the markings on the board showing the color of the end wires.

- Keypad P3

- Mode switches P4, and inventory payout P202.

- Coin Mechanism P404 (3bd) or P205 (2bd).

- Power P206 rectangular plug.

Now remove the connectors from the old boards and then remove the old boards. Position the new board and drill new holes for mounting screws. Be careful of interference with the gum and mint tray. Attach the connectors.

4900 Single board installation

Take a moment to study the replacement board looking for connectors labeled SB. Install the 6 standoffs in the board. You may want to label the connectors as you remove them from the old boards.

Locate these connectors on the replacement board:

- Display  P8

- Motors P10 and P11. Observe the markings on the board showing the color of the end wires.

- Keypad P9

- Mode switches P5.

- Coin Mechanism C300 P1 and P2. The C300 connector must be attached

- Power P12.

Remove the connectors from the old board and then remove the old board. Position the new board and drill new holes for mounting screws. Be careful of interference with the gum and mint tray. Attach the connectors.

Along the right edge of the board, below the red two wire BV connector find a 3 position connector covered with tubing. Remove the tubing and attach the 110V validator power cable from the parts bag. Attach the red and black wires to 110VAC. P303-1 and P303-3 are suggested.

Your

Text Here.

Installation test

How I test:

-Power the machine. Hear "beep" on power up (and BV cycle).

-About 3 seconds later 4 more beeps.

-Close the door switch. Listen for a single beep (operate mode).

-Release door switch hear 3 beeps (service mode).

-Press keypad keys, see display and hear beep. Press reset.

-On Remote press test vend. This will cycle all motors. Or select 1 motor first. Motor power led blinks on as motors run.

-Payout nickel, dime, quarter.

-Close door switch, insert coin and see credit.

Done

Features

-Beeper.

-Selection under price will show the item price for 3 seconds.

-$1 and $5 bill acceptance.

-Token and coupon free vend.

-Debit card.

-Optional Tru-Vend guarenteed delivery detection system.

-MDB coin mech with $1 coin payout.

-Internal sales meter.

-Change payout countdown

-Stutter (motor will stutter beginning about 2/3s of cycle).

Operate mode

-Blinking decimal point shows machine ready to take money.

Service mode

-Selection+Enter Price button = enter price.

-Inventory payout .25, .10, .05

-Test vend with selection will run that motor.

-Test vend button with no selection will run that motor.

-Test vend button with 1 selection will run that shelf.

-Enter load button = sales meter. Cents on bottom $ on top. Ends with led test.

Removed Features

-C300 support. Connector still needed.

-Enter product load (now sales meter) and load count.

-Diagnostic clear and codes.

Credit +99 +test vend = run motors at that price.

MDB Devices:

Use optional MDB harness kit VH192

With an MDB coin mechanism you may use either a “pulse” validator or an MDB validator.

MDB bill validator:

In addition to the comments about the 110V validator, with the MDB version the $5 enable switch should be thought of as “all bills” (vs low bill). That is if you set the BV switch’s to allow a $10, it will accept as long as the conditions are ok for the 5. To use the coupon free vend, the $5 accept switch must be on.

MDB coin mechanism:

MDB coin mechanisms count coins. The various manufactures and generations work differently with power off and cassette removal. The coin count is used to enable the bill validator and correct change light. Another problem is that MDB coin mechanisms do not pay air. If the validator does not enable, you may need to vend in some coins. Token free vend is supported.

To payout coins, use the buttons on the coin mechanism.

Mexican coin mechanisms:

If a Mexican coin mechanism is attached, in the single board machine with the 4 digit display, coins will display as actual value. When pricing the machine enter prices divided by ten.  That is, for a 5P price enter .50. That price will later display as 5.00.

The 3 board machine shows the value divided by 10.  5P will show as .50.

Bill Acceptor

110V Validator should be configured for long pulse (7 and 8 off).

The $1 acceptance is controlled by the quarter and nickel low tube sensors. If the $5 accept dip switch is on, $5 acceptance is controlled by board coin count showing more than $12.75 in the coin tubes.

The board has a BV enable led. The led has 4 possible states:

On steady 	BV bill(s) enabled.

Off 		BV inhibided.

Slow blink	BV inhibited - low quarter or nickel tube.

Fast blink	$5 Dip sw on & $5 inhibited - less than $12.75

The blinking is at the same rate as the display. If the BV enable is fast blinking, the display will also fast blink as an external indication.

Note: on logic mechs -if tubes are filled manually, the internal coin count will be revised to high tube value as soon as a coin of that value is routed to the cash box. So fill the tubes, then vend in 1 of each coin.  Tube values are calculated every 5 seconds.

To enable escrow, turn on the dip switch.

An optional harness VH227, is available to use a Coinco BA30.  Because this is a high level interface, the validator will never stop taking bills. No credit will be lost. Escrow is not supported.

Troubleshooting

-No beep on power up. If no +5 led check power plug. If +5 led ok possible bad board. Remove all connections but power and try again.

-No beep when door switch is cycled, bad door switch. (4 last year)

-Beeper squeels. No coin mech. Recheck connectors and coin mech.

(rare-3 board with C300, orange wire missing from P205 [ now attached to a 1 pin terminal]- move orange wire to pin 7 of P205). (Rowe schematic shows pin 9 incorrectly).

-No inventory payout (and no BV cycle in 3 board) -check 110VAC

-No inventory payout (3bd). Check 110V DC at two right end wires of P205 connector.

-No motors. Motor power led does flash. Check long connector orientation. No led check 24VAC

Greenwick Inc.

610-857-5910 9-4 ET